## Slide 1
October 20, 2022
Python in the Built Environment
Dalton Goodwin

## Slide 2
October 20, 2022
High-level programming language
Often used to build websites, software, automate tasks, and conduct data analysis
Use as a scripting or glue language to connect existing components together https://www.python.org/doc/essays/blurb/
Introduction
Dalton Goodwin
Work at Henderson Engineers
Retail BIM TM (Technical Manager)
Have used Python for 4+ years
Working with design technology 6+ years
Experience in Architecture and Engineering

## Slide 3
October 20, 2022
High-level programming language
Often used to build websites, software, automate tasks, and conduct data analysis
Use as a scripting or glue language to connect existing components together https://www.python.org/doc/essays/blurb/
Class Goals:
Inspire you to learn Python!
Show you some practical real examples
Give you ideas on how you can use Python

## Slide 4
October 20, 2022
What is Python, and why does it matter?
Example 3: Visualizing Clash Data
Example 1: Duct Pressure Loss
Example 2: BIM Spent Report
Agenda
Wrap-up and resources
High-level programming language
Often used to build websites, software, automate tasks, and conduct data analysis
Use as a scripting or glue language to connect existing components together https://www.python.org/doc/essays/blurb/

## Slide 5: What is Python?
High-level programming language
Often used to build websites, software, automate tasks, and conduct data analysis
Use as a scripting or glue language to connect existing components together https://www.python.org/doc/essays/blurb/
What is Python, and why does it matter?
Example 3: Visualizing Clash Data
Example 1: Duct Pressure Loss
Example 2: BIM Spent Report
Wrap-up and resources
Why does it matter?
Many tools can be extended with code/low-code
Allow unique automation/processes not available through UI
Make life easier!
Notes: Assembly and C are lower-level languages
Python is very similar to English!
Python is a high-level programming language designed to be easy to read and simple to implement. It is open source, which means it is free to use, even for commercial applications. Python can run on Mac, Windows, and Unix systems and has also been ported to Java and .NET virtual machines.
Python is a computer programming language often used to build websites and software, automate tasks, and conduct data analysis. Python is a general purpose language, meaning it can be used to create a variety of different programs and isn’t specialized for any specific problems. This versatility, along with its beginner-friendliness, has made it one of the most-used programming languages today.

## Slide 6: Why does it matter?
Many tools can be extended with code/low-code
Allow unique automation/processes not available through UI
Connect different tools
Make life easier with code!
Python Popularity
Notes: Many tools can be extended with code/low-code
Grashopper
Dynamo
Revit
Allow unique automation/processes that leverage API functionality not available through the UI.
Duct module tool example
Fabrication example (Rods length)

## Slide 7
Python Popularity
Why does it matter?
Many tools can be extended with code/low-code
Allow unique automation/processes not available through UI
Make life easier!
Notes: TIOBE Index: TIOBE ratings are calculated by counting hits of the most popular search engines. Twenty-five search engines are used to calculate the TIOBE index. The TIOBE Programming Community index is an indicator of the popularity of programming languages. The index started in the year 2001 and updated once a month.
PYPL Index: The PYPL PopularitY of Programming Language Index is created by analyzing how often language tutorials are searched on Google. The index is updated once a month.
https://statisticstimes.com/tech/top-computer-languages.php

## Slide 8
https://statisticstimes.com/tech/top-computer-languages.php
Python Popularity
Notes: TIOBE Index: TIOBE ratings are calculated by counting hits of the most popular search engines. Twenty-five search engines are used to calculate the TIOBE index. The TIOBE Programming Community index is an indicator of the popularity of programming languages. The index started in the year 2001 and updated once a month.
PYPL Index: The PYPL PopularitY of Programming Language Index is created by analyzing how often language tutorials are searched on Google. The index is updated once a month.
https://statisticstimes.com/tech/top-computer-languages.php

## Slide 9
https://statisticstimes.com/tech/top-computer-languages.php
What is Python, and why does it matter?
Example 3: Visualizing Clash Data
Example 1: Duct Pressure Loss
Example 2: BIM Spent Report
Wrap-up and resources
Notes: TIOBE Index: TIOBE ratings are calculated by counting hits of the most popular search engines. Twenty-five search engines are used to calculate the TIOBE index. The TIOBE Programming Community index is an indicator of the popularity of programming languages. The index started in the year 2001 and updated once a month.
PYPL Index: The PYPL PopularitY of Programming Language Index is created by analyzing how often language tutorials are searched on Google. The index is updated once a month.
https://statisticstimes.com/tech/top-computer-languages.php

## Slide 10
October 20, 2022
What is Python, and why does it matter?
Example 3: Visualizing Clash Data
Example 1: Duct Pressure Loss
Example 2: BIM Spent Report
Agenda
Wrap-up and resources
October 20, 2022
Example 1 of 3: Duct Pressure Loss (Dynamo and Python) Automation
Goal: To save time for the designer

## Slide 11
October 20, 2022
Example 1 of 3: Duct Pressure Loss (Dynamo and Python) Automation
Goal: To save time for the designer
What is Duct Pressure Loss?
Air resistance grows directly proportional to air flow. This phenomenon is known as pressure loss.
https://ventilation-system.com/what-is-pressure-loss
Can we automate this?!
Notes: This was to support a longer term of getting people into projects
Ensure system is fully closed
CFM filled in on all diffusers
Cap all open ends
Show disconnects
Check duct systems

## Slide 12
October 20, 2022
1
2
3
Can we automate this?!
Example 1 of 3: Duct Pressure Loss (Dynamo and Python) Automation
Goal: To save time for the designer
Notes: This was to support a longer term of getting people into projects
Ensure system is fully closed
CFM filled in on all diffusers
Cap all open ends
Show disconnects
Check duct systems

## Slide 13
October 20, 2022
What is Duct Pressure Loss?
Air resistance grows directly proportional to air flow. This phenomenon is known as pressure loss.
https://ventilation-system.com/what-is-pressure-loss
Example 1 of 3: Duct Pressure Loss (Dynamo and Python) Automation
Goal: To save time for the designer
Live Demo 1 of 3: Duct Pressure Loss (Dynamo and Python) Automation
October 20, 2022
1
2
3
Can we automate this?!
Notes: This was to support a longer term of getting people into projects
Ensure system is fully closed
CFM filled in on all diffusers
Cap all open ends
Show disconnects
Check duct systems
As air moves through a duct the air closest to the duct moves slower than air in middle of the duct due to friction. The friction impacts a static pressure drop that a fan needs to overcome to move air through the duct. We can calculate that pressure drop by knowing the air flow, the dimensions of the duct and the length of the duct run at that size. Every elbow, transition, takeoff, or other fitting on a duct run will also have a static pressure impact. We utilize formulas within a design standard (SMACNA) to help us determine what that static pressure value is.
Fans use electrical power to create a pressure differential across themselves (potential energy). This pressure differential causes air to flow down a duct (kinetic energy). As air travels down the duct obstructions will cause turbulence. Also, air moving against the inside of the duct will create friction. Both effects cause the available pressure (potential energy) to be reduced. This reduction in available pressure is called a “pressure drop” and we can calculate how much pressure is lost from each obstruction, transition, elbow, etc.

## Slide 14
October 20, 2022
1
2
3
What is Duct Pressure Loss?
Air resistance grows directly proportional to air flow. This phenomenon is known as pressure loss.
https://ventilation-system.com/what-is-pressure-loss
Example 1 of 3: Duct Pressure Loss (Dynamo and Python) Automation
Goal: To save time for the designer
Do you need to learn to code?
I don’t think so!
Knowing when to speak up about an ineffective or inefficient process is just as important
Many wonderful visual tools available
Notes: This was to support a longer term of getting people into projects
Ensure system is fully closed
CFM filled in on all diffusers
Cap all open ends
Show disconnects
Check duct systems

## Slide 15
October 20, 2022
Actionable Takeaways:
Encourage “better” Revit modeling with automation
Create a communication channel for automation
Automating part of the process is the first step
Don’t be limited by the tools. Use the right tool for the job
Notes: This was to support a longer term of getting people into projects
Ensure system is fully closed
CFM filled in on all diffusers
Cap all open ends
Show disconnects
Check duct systems
As air moves through a duct the air closest to the duct moves slower than air in middle of the duct due to friction. The friction impacts a static pressure drop that a fan needs to overcome to move air through the duct. We can calculate that pressure drop by knowing the air flow, the dimensions of the duct and the length of the duct run at that size. Every elbow, transition, takeoff, or other fitting on a duct run will also have a static pressure impact. We utilize formulas within a design standard (SMACNA) to help us determine what that static pressure value is.
Fans use electrical power to create a pressure differential across themselves (potential energy). This pressure differential causes air to flow down a duct (kinetic energy). As air travels down the duct obstructions will cause turbulence. Also, air moving against the inside of the duct will create friction. Both effects cause the available pressure (potential energy) to be reduced. This reduction in available pressure is called a “pressure drop” and we can calculate how much pressure is lost from each obstruction, transition, elbow, etc.

## Slide 16
October 20, 2022
What is Python, and why does it matter?
Example 3: Visualizing Clash Data
Example 1: Duct Static Loss
Example 2: BIM Spent Report
Agenda
Wrap-up and resources
Example 2 of 3 : BIM Spent Report (Python and Power Bi)
Goal: To learn how Revit and AutoCAD are used
Example 2 of 3 : BIM Spent Report (Python and Power Bi)
Goal: To learn how Revit and AutoCAD are used
This will help guide our decisions across the sector
The data can be used to help show the success of Revit and automation
The data can be used to make sure we are heading to our goal of full Revit

## Slide 17
October 20, 2022
Example 2 of 3 : BIM Spent Report (Python and Power Bi)
Goal: To learn how Revit and AutoCAD are used
This will help guide our decisions across the sector
The data can be used to help show the success of Revit and automation
The data can be used to make sure we are heading to our goal of full Revit
Notes: This was to support a longer term of getting people into projects
Jupyter notebook is a wonderful way to show the thought process

## Slide 18
October 20, 2022
Example 2 of 3 : BIM Spent Report (Python and Power Bi)
Goal: To learn how Revit and AutoCAD are used
Notes: This was to support a longer term of getting people into projects
Jupyter notebook is a wonderful way to show the thought process

## Slide 19
October 20, 2022
Example 2 of 3 : BIM Spent Report (Python and Power Bi)
Goal: To learn how Revit and AutoCAD are used
Data Used:
Labor spent
Software usage (Revit and AutoCAD)
Per person on project
Project numbers
Project_software
Notes: This was to support a longer term of getting people into projects
Jupyter notebook is a wonderful way to show the thought process

## Slide 20
October 20, 2022
Example 2 of 3 : BIM Spent Report (Python and Power Bi)
Goal: To learn how Revit and AutoCAD are used
Data Used:
Labor spent
Software usage (Revit and AutoCAD)
Per person on project
Project numbers
Project_software
Notes: This was to support a longer term of getting people into projects
Jupyter notebook is a wonderful way to show the thought process

## Slide 21
October 20, 2022
Data Used:
Labor spent (Labor db SQL)
Software usage (Usage db SQL)
Per person on project
Project numbers (Project db SQL)
Project_software (Custom data)
Notes: This was to support a longer term of getting people into projects
Ensure system is fully closed
CFM filled in on all diffusers
Cap all open ends
Show disconnects
Check duct systems
As air moves through a duct the air closest to the duct moves slower than air in middle of the duct due to friction. The friction impacts a static pressure drop that a fan needs to overcome to move air through the duct. We can calculate that pressure drop by knowing the air flow, the dimensions of the duct and the length of the duct run at that size. Every elbow, transition, takeoff, or other fitting on a duct run will also have a static pressure impact. We utilize formulas within a design standard (SMACNA) to help us determine what that static pressure value is.
Fans use electrical power to create a pressure differential across themselves (potential energy). This pressure differential causes air to flow down a duct (kinetic energy). As air travels down the duct obstructions will cause turbulence. Also, air moving against the inside of the duct will create friction. Both effects cause the available pressure (potential energy) to be reduced. This reduction in available pressure is called a “pressure drop” and we can calculate how much pressure is lost from each obstruction, transition, elbow, etc.

## Slide 22
October 20, 2022
Data Used:
Labor spent (Labor db SQL)
Software usage (Usage db SQL)
Per person on project
Project numbers (Project db SQL)
Project_software (Custom data)
Notes: This was to support a longer term of getting people into projects
Ensure system is fully closed
CFM filled in on all diffusers
Cap all open ends
Show disconnects
Check duct systems
As air moves through a duct the air closest to the duct moves slower than air in middle of the duct due to friction. The friction impacts a static pressure drop that a fan needs to overcome to move air through the duct. We can calculate that pressure drop by knowing the air flow, the dimensions of the duct and the length of the duct run at that size. Every elbow, transition, takeoff, or other fitting on a duct run will also have a static pressure impact. We utilize formulas within a design standard (SMACNA) to help us determine what that static pressure value is.
Fans use electrical power to create a pressure differential across themselves (potential energy). This pressure differential causes air to flow down a duct (kinetic energy). As air travels down the duct obstructions will cause turbulence. Also, air moving against the inside of the duct will create friction. Both effects cause the available pressure (potential energy) to be reduced. This reduction in available pressure is called a “pressure drop” and we can calculate how much pressure is lost from each obstruction, transition, elbow, etc.

## Slide 23
October 20, 2022
Data Used:
Labor spent (Labor db SQL)
Software usage (Usage db SQL)
Per person on project
Project numbers (Project db SQL)
Project_software (Custom data)
Notes: This was to support a longer term of getting people into projects
Ensure system is fully closed
CFM filled in on all diffusers
Cap all open ends
Show disconnects
Check duct systems
As air moves through a duct the air closest to the duct moves slower than air in middle of the duct due to friction. The friction impacts a static pressure drop that a fan needs to overcome to move air through the duct. We can calculate that pressure drop by knowing the air flow, the dimensions of the duct and the length of the duct run at that size. Every elbow, transition, takeoff, or other fitting on a duct run will also have a static pressure impact. We utilize formulas within a design standard (SMACNA) to help us determine what that static pressure value is.
Fans use electrical power to create a pressure differential across themselves (potential energy). This pressure differential causes air to flow down a duct (kinetic energy). As air travels down the duct obstructions will cause turbulence. Also, air moving against the inside of the duct will create friction. Both effects cause the available pressure (potential energy) to be reduced. This reduction in available pressure is called a “pressure drop” and we can calculate how much pressure is lost from each obstruction, transition, elbow, etc.

## Slide 24
October 20, 2022
Data Used:
Labor spent (Labor db SQL)
Software usage (Usage db SQL)
Per person on project
Project numbers (Project db SQL)
Project_software (Custom data)
Notes: This was to support a longer term of getting people into projects
Ensure system is fully closed
CFM filled in on all diffusers
Cap all open ends
Show disconnects
Check duct systems
As air moves through a duct the air closest to the duct moves slower than air in middle of the duct due to friction. The friction impacts a static pressure drop that a fan needs to overcome to move air through the duct. We can calculate that pressure drop by knowing the air flow, the dimensions of the duct and the length of the duct run at that size. Every elbow, transition, takeoff, or other fitting on a duct run will also have a static pressure impact. We utilize formulas within a design standard (SMACNA) to help us determine what that static pressure value is.
Fans use electrical power to create a pressure differential across themselves (potential energy). This pressure differential causes air to flow down a duct (kinetic energy). As air travels down the duct obstructions will cause turbulence. Also, air moving against the inside of the duct will create friction. Both effects cause the available pressure (potential energy) to be reduced. This reduction in available pressure is called a “pressure drop” and we can calculate how much pressure is lost from each obstruction, transition, elbow, etc.

## Slide 25
October 20, 2022
Data Used:
Labor spent (Labor db SQL)
Software usage (Usage db SQL)
Per person on project
Project numbers (Project db SQL)
Project_software (Custom data)
Notes: This was to support a longer term of getting people into projects
Ensure system is fully closed
CFM filled in on all diffusers
Cap all open ends
Show disconnects
Check duct systems
As air moves through a duct the air closest to the duct moves slower than air in middle of the duct due to friction. The friction impacts a static pressure drop that a fan needs to overcome to move air through the duct. We can calculate that pressure drop by knowing the air flow, the dimensions of the duct and the length of the duct run at that size. Every elbow, transition, takeoff, or other fitting on a duct run will also have a static pressure impact. We utilize formulas within a design standard (SMACNA) to help us determine what that static pressure value is.
Fans use electrical power to create a pressure differential across themselves (potential energy). This pressure differential causes air to flow down a duct (kinetic energy). As air travels down the duct obstructions will cause turbulence. Also, air moving against the inside of the duct will create friction. Both effects cause the available pressure (potential energy) to be reduced. This reduction in available pressure is called a “pressure drop” and we can calculate how much pressure is lost from each obstruction, transition, elbow, etc.

## Slide 26
Notes: This was to support a longer term of getting people into projects
Ensure system is fully closed
CFM filled in on all diffusers
Cap all open ends
Show disconnects
Check duct systems
As air moves through a duct the air closest to the duct moves slower than air in middle of the duct due to friction. The friction impacts a static pressure drop that a fan needs to overcome to move air through the duct. We can calculate that pressure drop by knowing the air flow, the dimensions of the duct and the length of the duct run at that size. Every elbow, transition, takeoff, or other fitting on a duct run will also have a static pressure impact. We utilize formulas within a design standard (SMACNA) to help us determine what that static pressure value is.
Fans use electrical power to create a pressure differential across themselves (potential energy). This pressure differential causes air to flow down a duct (kinetic energy). As air travels down the duct obstructions will cause turbulence. Also, air moving against the inside of the duct will create friction. Both effects cause the available pressure (potential energy) to be reduced. This reduction in available pressure is called a “pressure drop” and we can calculate how much pressure is lost from each obstruction, transition, elbow, etc.

## Slide 27
October 20, 2022
Notes: This was to support a longer term of getting people into projects
Ensure system is fully closed
CFM filled in on all diffusers
Cap all open ends
Show disconnects
Check duct systems
As air moves through a duct the air closest to the duct moves slower than air in middle of the duct due to friction. The friction impacts a static pressure drop that a fan needs to overcome to move air through the duct. We can calculate that pressure drop by knowing the air flow, the dimensions of the duct and the length of the duct run at that size. Every elbow, transition, takeoff, or other fitting on a duct run will also have a static pressure impact. We utilize formulas within a design standard (SMACNA) to help us determine what that static pressure value is.
Fans use electrical power to create a pressure differential across themselves (potential energy). This pressure differential causes air to flow down a duct (kinetic energy). As air travels down the duct obstructions will cause turbulence. Also, air moving against the inside of the duct will create friction. Both effects cause the available pressure (potential energy) to be reduced. This reduction in available pressure is called a “pressure drop” and we can calculate how much pressure is lost from each obstruction, transition, elbow, etc.

## Slide 28
October 20, 2022
Data Used:
Labor spent
Software usage (Revit and AutoCAD)
Per person on project
Project numbers
Project_software
Notes: This was to support a longer term of getting people into projects
Ensure system is fully closed
CFM filled in on all diffusers
Cap all open ends
Show disconnects
Check duct systems
As air moves through a duct the air closest to the duct moves slower than air in middle of the duct due to friction. The friction impacts a static pressure drop that a fan needs to overcome to move air through the duct. We can calculate that pressure drop by knowing the air flow, the dimensions of the duct and the length of the duct run at that size. Every elbow, transition, takeoff, or other fitting on a duct run will also have a static pressure impact. We utilize formulas within a design standard (SMACNA) to help us determine what that static pressure value is.
Fans use electrical power to create a pressure differential across themselves (potential energy). This pressure differential causes air to flow down a duct (kinetic energy). As air travels down the duct obstructions will cause turbulence. Also, air moving against the inside of the duct will create friction. Both effects cause the available pressure (potential energy) to be reduced. This reduction in available pressure is called a “pressure drop” and we can calculate how much pressure is lost from each obstruction, transition, elbow, etc.

## Slide 29
October 20, 2022
Data Used:
Labor spent
Software usage (Revit and AutoCAD)
Per person on project
Project numbers
Project_software
Notes: This was to support a longer term of getting people into projects
Ensure system is fully closed
CFM filled in on all diffusers
Cap all open ends
Show disconnects
Check duct systems
As air moves through a duct the air closest to the duct moves slower than air in middle of the duct due to friction. The friction impacts a static pressure drop that a fan needs to overcome to move air through the duct. We can calculate that pressure drop by knowing the air flow, the dimensions of the duct and the length of the duct run at that size. Every elbow, transition, takeoff, or other fitting on a duct run will also have a static pressure impact. We utilize formulas within a design standard (SMACNA) to help us determine what that static pressure value is.
Fans use electrical power to create a pressure differential across themselves (potential energy). This pressure differential causes air to flow down a duct (kinetic energy). As air travels down the duct obstructions will cause turbulence. Also, air moving against the inside of the duct will create friction. Both effects cause the available pressure (potential energy) to be reduced. This reduction in available pressure is called a “pressure drop” and we can calculate how much pressure is lost from each obstruction, transition, elbow, etc.

## Slide 30
October 20, 2022
Actionable Takeaways:
Python can connect your different data sources
Many tools have Python integrations
Make data more accessible with Power BI and Python
Notes: This was to support a longer term of getting people into projects
Ensure system is fully closed
CFM filled in on all diffusers
Cap all open ends
Show disconnects
Check duct systems
As air moves through a duct the air closest to the duct moves slower than air in middle of the duct due to friction. The friction impacts a static pressure drop that a fan needs to overcome to move air through the duct. We can calculate that pressure drop by knowing the air flow, the dimensions of the duct and the length of the duct run at that size. Every elbow, transition, takeoff, or other fitting on a duct run will also have a static pressure impact. We utilize formulas within a design standard (SMACNA) to help us determine what that static pressure value is.
Fans use electrical power to create a pressure differential across themselves (potential energy). This pressure differential causes air to flow down a duct (kinetic energy). As air travels down the duct obstructions will cause turbulence. Also, air moving against the inside of the duct will create friction. Both effects cause the available pressure (potential energy) to be reduced. This reduction in available pressure is called a “pressure drop” and we can calculate how much pressure is lost from each obstruction, transition, elbow, etc.

## Slide 31
October 20, 2022
What is Python, and why does it matter?
Example 3: Visualizing Clash Data
Example 1: Duct Static Loss
Example 2: BIM Spent Report
Agenda
Wrap-up and resources
Example 3 of 3: Visualizing Clash Detection Data (Python)
Goal: Gain a better understanding of clashes on a project

## Slide 32
October 20, 2022
Example 3 of 3: Visualizing Clash Detection Data (Python)
Goal: Gain a better understanding of clashes on a project
Notes: Revit, Dynamo, and Navisworks also used in this process.

## Slide 33
October 20, 2022
Example 3 of 3: Visualizing Clash Detection Data (Python)
Goal: Gain a better understanding of clashes on a project
Notes: Revit, Dynamo, and Navisworks also used in this process.

## Slide 34
Notes: This was to support a longer term of getting people into projects
Ensure system is fully closed
CFM filled in on all diffusers
Cap all open ends
Show disconnects
Check duct systems
As air moves through a duct the air closest to the duct moves slower than air in middle of the duct due to friction. The friction impacts a static pressure drop that a fan needs to overcome to move air through the duct. We can calculate that pressure drop by knowing the air flow, the dimensions of the duct and the length of the duct run at that size. Every elbow, transition, takeoff, or other fitting on a duct run will also have a static pressure impact. We utilize formulas within a design standard (SMACNA) to help us determine what that static pressure value is.
Fans use electrical power to create a pressure differential across themselves (potential energy). This pressure differential causes air to flow down a duct (kinetic energy). As air travels down the duct obstructions will cause turbulence. Also, air moving against the inside of the duct will create friction. Both effects cause the available pressure (potential energy) to be reduced. This reduction in available pressure is called a “pressure drop” and we can calculate how much pressure is lost from each obstruction, transition, elbow, etc.

## Slide 35
Notes: This was to support a longer term of getting people into projects
Ensure system is fully closed
CFM filled in on all diffusers
Cap all open ends
Show disconnects
Check duct systems
As air moves through a duct the air closest to the duct moves slower than air in middle of the duct due to friction. The friction impacts a static pressure drop that a fan needs to overcome to move air through the duct. We can calculate that pressure drop by knowing the air flow, the dimensions of the duct and the length of the duct run at that size. Every elbow, transition, takeoff, or other fitting on a duct run will also have a static pressure impact. We utilize formulas within a design standard (SMACNA) to help us determine what that static pressure value is.
Fans use electrical power to create a pressure differential across themselves (potential energy). This pressure differential causes air to flow down a duct (kinetic energy). As air travels down the duct obstructions will cause turbulence. Also, air moving against the inside of the duct will create friction. Both effects cause the available pressure (potential energy) to be reduced. This reduction in available pressure is called a “pressure drop” and we can calculate how much pressure is lost from each obstruction, transition, elbow, etc.

## Slide 36
October 20, 2022
Actionable Takeaways:
Use Python to view data in creative and interesting ways
Notes: This was to support a longer term of getting people into projects
Ensure system is fully closed
CFM filled in on all diffusers
Cap all open ends
Show disconnects
Check duct systems
As air moves through a duct the air closest to the duct moves slower than air in middle of the duct due to friction. The friction impacts a static pressure drop that a fan needs to overcome to move air through the duct. We can calculate that pressure drop by knowing the air flow, the dimensions of the duct and the length of the duct run at that size. Every elbow, transition, takeoff, or other fitting on a duct run will also have a static pressure impact. We utilize formulas within a design standard (SMACNA) to help us determine what that static pressure value is.
Fans use electrical power to create a pressure differential across themselves (potential energy). This pressure differential causes air to flow down a duct (kinetic energy). As air travels down the duct obstructions will cause turbulence. Also, air moving against the inside of the duct will create friction. Both effects cause the available pressure (potential energy) to be reduced. This reduction in available pressure is called a “pressure drop” and we can calculate how much pressure is lost from each obstruction, transition, elbow, etc.

## Slide 37
October 20, 2022
What is Python, and why does it matter?
Example 3: Visualizing Clash Data
Example 1: Duct Static Loss
Example 2: BIM Spent Report
Agenda
Wrap-up and resources

## Slide 38: Do you need to learn to code?
I don’t think so! But it can help
Knowing when to speak up about an ineffective or inefficient process is just as important
Many excellent visual low code/no code tools are available
Notes: Many tools can be extended with code/low-code
Grashopper
Dynamo
Revit
Allow unique automation/processes that leverage API functionality not available through the UI.
Duct module tool example
Fabrication example (Rods length)

## Slide 39: Visual low code/no code tools
KNIME
Dynamo
Excel
Grasshopper
SQL
Power BI
Notes: Many tools can be extended with code/low-code
Grashopper
Dynamo
Revit
Allow unique automation/processes that leverage API functionality not available through the UI.
Duct module tool example
Fabrication example (Rods length)

## Slide 40: Where can you use Python?
KNIME
Grasshopper
Dynamo
SQL
Excel
Power BI
Notes: Many tools can be extended with code/low-code
Grashopper
Dynamo
Revit
Allow unique automation/processes that leverage API functionality not available through the UI.
Duct module tool example
Fabrication example (Rods length)

## Slide 41
October 20, 2022
Resources for learning Python:
Python Tutor:
https://pythontutor.com/visualize.html#mode=edit
KNIME
Grasshopper
Dynamo
SQL
Excel
Power BI

## Slide 42
October 20, 2022
Resources for learning Python:
LinkedIn Learning – Python Quick Start:
https://www.linkedin.com/learning/python-quick-start/advance-your-career-with-python

## Slide 43
October 20, 2022
Resources for learning Python:
Codewars: https://www.codewars.com/dashboard

## Slide 44
October 20, 2022
Contact Information:
GitHub: https://github.com/DaltonGOO
LinkedIn: https://www.linkedin.com/in/dalton-goodwin-067a07107/
YouTube: https://www.youtube.com/c/TheBIMCoordinator/featured
Notes: This was to support a longer term of getting people into projects
Ensure system is fully closed
CFM filled in on all diffusers
Cap all open ends
Show disconnects
Check duct systems
As air moves through a duct the air closest to the duct moves slower than air in middle of the duct due to friction. The friction impacts a static pressure drop that a fan needs to overcome to move air through the duct. We can calculate that pressure drop by knowing the air flow, the dimensions of the duct and the length of the duct run at that size. Every elbow, transition, takeoff, or other fitting on a duct run will also have a static pressure impact. We utilize formulas within a design standard (SMACNA) to help us determine what that static pressure value is.
Fans use electrical power to create a pressure differential across themselves (potential energy). This pressure differential causes air to flow down a duct (kinetic energy). As air travels down the duct obstructions will cause turbulence. Also, air moving against the inside of the duct will create friction. Both effects cause the available pressure (potential energy) to be reduced. This reduction in available pressure is called a “pressure drop” and we can calculate how much pressure is lost from each obstruction, transition, elbow, etc.

## Slide 49
Conditional Statements